## Slide 1: BACnet Secure Connect - A Cyber Resilience Foundation for Building Automation

## Slide 2
Buildings in the past: Local
Isolated OT communications
Mainly local operation
Little attack surface
Buildings today: Connected
Converged IT↔OT
Cloud + Mobile Operation
Increased attack surface

## Slide 3
Cybersecurity is not an “option” anymore!
Source: KNX-board E-Mail-Distribution list, Nov’21
The list of incidents is growing.
Attacks to BAC are reality.
Cybersecurity if a key success
factor for our business today.
Notes: Attacks to BACS are reality
The recent KNX-organization’s “call for experts” is just the most recent example in a dramatically growing list of incidents
Today, cybersecurity is a key success factor for our business

## Slide 4
Cybersecurity is not an “option” anymore!
Source: https://www.forescout.com/resources/project-memoria-lookback-report/ , Nov’21
IT-researchers actively scan BACS for cybersecurity issues.
Caring for cybersecurity becomes an asset.
Cybersecurity if a key success
factor for our business today.
«Among all the vendors, Siemens is the only one that has publicly stated to be affected by the vulnerabilities in all the disclosure phases. So far, Siemens has issued 12 advisories based on Project Memoria’s findings. Siemens is also the vendor that issued 31% of ICS-CERT alerts in 2020.»
«This is not a coincidence and is far from implying that Siemens’ devices are less secure than others. On the contrary, it shows that they have a mature product security program and that they are open to acknowledging and publishing issues that affect their products.
It also indicates that several other similar vendors have not taken the same proactive approach and may be leaving their customers vulnerable.»
Notes: “Among all the vendors, Siemens is the only one that has publicly stated to be affected by the vulnerabilities in all the disclosure phases. So far, Siemens has issued 12 advisories based on Project Memoria’s findings. Siemens is also the vendor that issued 31% of ICS-CERT alerts in 2020.
This is not a coincidence and is far from implying that Siemens’ devices are less secure than others. On the contrary, it shows that they have a mature product security program and that they are open to acknowledging and publishing issues that affect their products.
It also indicates that several other similar vendors have not taken the same proactive approach and may be leaving their customers vulnerable.”

## Slide 5
Social engineering
Lower-level exploits against device firmware
Ransomware
Phishing
Building automation
protocols
DDoS attack
  Malware infection
BACnet dates back to 1987:
  No encryption → no privacy
  No authentication → not tamper-proof
Used in around ~70% of all commercial BACS
Huge installed base → stepwise migration option needed
  Remote attacks
Many Ways to attack a Building..

## Slide 6
Many Ways to attack a Building..
..and a way to fight back
Encrypted traffic
Authenticated devices
Backward compatible
IT-friendly
  Approved and released in November 2019
Notes: BACnet dates back to 1987:
  No encryption → no privacy
  No authentication → not tamper-proof
Used in around ~70% of all commercial BACS
Huge installed base → stepwise migration option needed

## Slide 7
A new BACnet datalink (like BACnet MS/TP or BACnet/IP)
A traffic encryption to prevent the M2M-communication against tampering
An authentication mechanism to restrict access to a project
An IT-friendly way to do secure Building Automation communication
What BACnet/SC is
A silver bullet against all kinds of cybersecurity risks
A fine-granular authorization mechanism
Something that provides IT security “free of charge”..
What BACnet/SC is not
BACnet Secure Connect (“BACnet/SC”)

## Slide 8
Investment protection: Backward compatibility and step-wise migration / extension
Privacy: Secure end-to-end communication in insecure network environments
Protection: Rule out rogue devices and Men-in-the-Middle attacks (MitM)
Cost efficient: Blend nicely into existing “IT mainstream” landscape
Value Proposition
BACnet Secure Connect (“BACnet/SC”)
A new BACnet datalink (like BACnet MS/TP or BACnet/IP)
A traffic encryption to prevent the M2M-communication against tampering
An authentication mechanism to restrict access to a project
An IT-friendly way to do secure Building Automation communication
What BACnet/SC is

## Slide 9: What are the key functional benefits?
  Is another data link
  Application layer untouched
  Built on TLS 1.3, a sophisticated IT encryption standard
  Authenticates devices and users via X.509 certificates and PKI
  Does not depend on UDP-based network broadcast messaging
  Works easily with firewalls
  State-of-the-art security
  Using IT best practices
  More cost-efficient to cybersecure the system
  Secure end-to-end device communication possible via insecure IP networks
  Easy (step-wise) extension or migration of installed base
Key benefits
Key features

## Slide 10
BACnet Application Layer
BACnet Network Layer
BACnet Datalink
& Physical Layers
...
MS/TP
BACnet/IP
BACnet/SC
RS485
UDP/IPv4
WebSockets
...
BACnet Application
No impact upon application layer
Mix-and-match with other BACnet flavors
Realization / migration / extension on a granularity “per BACnet network”
Independent of BACnet revision (for the first time in history!)
Take-Aways
BACnet/SC Essentials
Backward Compatibility

## Slide 11: BACnet/SC Essentials Topology
/SC deploys a “hub-and-spoke” principle
  nodes = communication end-points
  hubs = central points to route traffic
  failover hubs = hot-standby redundancy
  encrypted web sockets used hub ↔ nodes
/SC is a new BACnet datalink
  connects by BACnet routing to /IP, /MSTP
  “hubs” typically also host “routers”
WebSocket
PrimaryHub
Failover Hub
Node
/IP Device
BACnet/SC
BACnet/IP
UDP
Node
Node
/SC ↔ /IP
Router
TCP
Node
Take-Aways

## Slide 12: BACnet/SC Essentials Topology
WebSocket
PrimaryHub
Failover Hub
Node
/IP Device
BACnet/SC
BACnet/IP
UDP
Node
Node
/SC ↔ /IP
Router
TCP
Node
Take-Aways
“hubs”, “nodes”, “routers” are all logical roles
  Must not correlate to physical devices
  For price-efficiency, a “hub” will typically also be a “router” (like our PXC5/7, too)
“hub-and-spoke” is a logical concept
  Must not correlate to physical cabling
  For price efficiency, projects often use daisy-chain cabling (and can continue to do so)

## Slide 13: BACnet/SC Essentials Topology
WebSocket
PrimaryHub
Control Point
PXC7
Node
PXC4
DXR2
PXC5
/IP Device
BACnet/SC
BACnet/IP
UDP
Node
Node
/SC ↔ /IP
Router
TCP
Failover Hub
CC
Node
Portfolios will stepwise extend to BACnet/SC
Projects will stepwise migrate to BACnet/SC
Devices shall support both BACnet/IP + /SC
Challenge to scale /SC interoperably to large systems (“local matter” by the standard)
Take-Aways
* Available for PXC and Desigo CC in the first step, others are on the roadmap

## Slide 14: BACnet/SC Essentials Certificates
Cybersecurity requires each /SC device to host two digital certificates
  A (common) “Root Certificate” “I’m a legit member of this network”
  An (individual) “Operational Certificate” “Only me can decrypt my traffic”
Handling of certificates is a key task in /SC
  Who issues/signs? Early definition needed!
  Who maintains? IT-staff or OT-staff?
  There will be only exactly one Signing CA for one BACnet/SC network!
Hub
Node
Node
Node
Node
Node
Node
1
7
6
2
3
4
5
x
Operational Certificate no. x (aka “Client Certificate")
Common Signing CA’s Root Certificate
(aka "Issuer Certificate“)
Take-Aways

## Slide 15: BACnet/SC Essentials Certification Authorities (“CA”)
Certification Authority
Real Life Analogy
Siemens Badge
Siemens Authority
“I claim being a legit Siemens employee”
“I can proof being John Doe at Siemens”
“I claim being John Doe”
check
check
certify
certify
BACnet/SC
“I claim being a legit device of this project”
“I claim being Node #42”
Root
Node 42
Project’s CA
“I can proof being Node 42 of this project”
check
check
certify
certify
Node 42
op42
CA is a trusted entity in a project
  Issues (common) root certificate
  Issues (individual) operational certificates
  There is exactly one such CA in a project → Needs alignment !
Certificates are mandatory for /SC
  Needed initially to E&C a site
  Need renewals over site lifetime
  Use IT-best practice (“X509.v3”, “TLS1.3”, “WebSockets”, ..)
Take-Aways

## Slide 16: BACnet/SC Essentials Certification Authorities (“CA”)
ABT Site is the Signing CA
Single Vendor Case
Certificates handled all by (and within) ABT Site
“Self-signed” certificates
Very easy workflows
Multi Vendor Case
Customer IT Case
3rd party tool is CA
ABT creates operational certificates for our equipment
3rd party creates root certif. and signs operational certif.
Export / import per files
Vendor tools interact with customer’s CA on a file basis
IT-signed certificates
Difficult at E&C times, tedious at O&M times..
ABT Site
ABT Site
3rd tool
End-customer’s own CA
ABT Site
3rd tool
Node x
opX
Root
Node y
opY
Root
Node x
opX
Root
Node x
opX
Root
Node y
opY
Root

## Slide 17: BACnet/SC Solutions Mixed Use Case /SC + /IP
/SC will come step-wise into projects
/SC will come step-wise into portfolio
“/SC ready” means: You can upgrade to /SC by FW upgrade (and re-engineering)
Extension / migration will happen on a “per BACnet network” granularity
IT network
OT network
Brownfield scenario
Node
Hub
IP/SC
Router
FailoverHub
Secure
BACnet
Unsecure
BACnet
Desigo CC 5.1
PXC5/7
Non
SC
Non
SC
PXC5/7
Non
SC
IT network
OT network
Node
Greenfield scenario
FailoverHub
Node
Node
Node
PXC5/7
IP/SC
Router
Hub
Non
SC
Non
SC
Take-Aways

## Slide 18: ASHRAE Road to BACnet Secure Connect Enhancements - Outlook
BACnet/SC Release
  November 2019
  ASHRAE Addendum bj to ASHRAE Standard 135-2016, Annex AB
Interoperable Security Configuration
  ~2022
  Addendum 135-2020cc and 135-2020cd
IT Friendliness and Security
  ASHRAE SSPC 135 IT-WG, 2009
  Work on BACnet/SC
Plug&Play
  ~2023
  Zero Touch Onboarding
  (IETF ANIMA BRSKI)
  Plug&Play Network Configuration for PKI
Authorization
~2023
  ASHRAE SSPC 135 NS-WG
  Work on User Authorization with OAuth2.0 Concepts
“Managed BACnet”
~2022
Multi-vendor initiative to align, started 2020
Work on many IT-best practices beyond /SC