Training Document for

Integrated Automation Solutions

Totally Integrated Automation (TIA)

Module S01

Fundamentals of CNC Programming

with SinuTrain

This document was prepared by Siemens AG for training purposes for the project 'Siemens Automation Cooperates with Education’ (SCE).

Siemens AG does not guarantee the content of this document.

Passing on this document, copying it and using and sharing its content is allowed within public training facilities and continued education facilities.  Exceptions require written approval by Siemens AG (Michael Knust michael.knust@siemens.com).

Offenders are held liable. All rights reserved, including translation rights, particularly in the event a patent is granted or a utility model or design is registered.

We thank the Michael Dziallas Engineering corporation, the teachers of vocational schools others for their support during the preparation of this document.

Table of Contents

1	Preface	5

2	Introduction	7

2.1	Development Phases of CNC Technology	7

2.2	Controller Requirements for the New Millennium	7

2.3	Advantages of CNC Programming with SinuTrain SHOPMILL, SHOPTURN	7

3	Programming a Turned Part in G-Code	8

4	Programming a Turned Part according to the Machining Step Procedure	9

4.1	Starting SINUTRAIN	9

4.2	Selecting the Machine	10

4.3	SINUTRAIN Basic Display	10

4.4	Generating the Turning Program	11

4.5	Setting Up a New Directory/Program Generation	11

4.6	Setting Up a New Workpiece Program	12

4.7	Program Header	13

4.8	Program Editor	14

4.9	Tool Selection	14

4.10	Face Turning	15

4.11	Workpiece Contour	17

4.12	Stock Removal Cycle Roughing	22

4.13	Finishing the Outside Contour	23

4.14	Thread Undercut	23

4.15	Thread Cutting	24

4.16	Making Grooves	25

4.17	Simulation	26

5	Programming a Milled Part in G-Code	28

6	Programming a Milled Part according to the Machining Step Process	31

6.1	Start SINUTRAIN	32

6.2	Selecting the Machine	32

6.3	SINUTRAIN Basic Display	32

6.4	Setting Up a New Directory/Program Generation	33

6.5	Setting Up a New Workpiece Program	34

6.6	Program Header	35

6.7	Outside Contour	36

6.8	Roughing the Outside Contour	37

6.9	Selecting the Tool	37

6.10	Finishing the Outside Contour	38

6.11	Stock Removal, Residual Material and Finishing of Contour Pockets and Inside Contour	39

6.12	Stock Removal of Contour Pocket Roughing	41

6.13	Removing Residual Material from the Corners	42

6.14	Finishing the Base	43

6.15	Finishing the Edge	44

6.16	Roughing the Circular Pocket Diameter 60	45

6.17	Finishing the Circular Pocket Diameter 60	45

6.18	Roughing the Circular Pocket Diameter 30	46

6.19	Finishing the Circular Pocket Diameter 30	46

6.20	Centering and Drilling taking Obstructions into Account	46

6.21	Machining Step Centering	46

6.22	Machining Step Drilling	47

6.23	Inputting the Line of Holes to the Left	47

6.24	First Obstruction	47

6.25	Inputting the Line of Holes to the Right	48

6.26	Second Obstruction	48

6.27	Drilling the Full Circle	48

6.28	Third Obstruction	48

6.29	Drilling a Single Hole	48

6.30	Simulation	49

7	Additional Tasks for Turning	50

7.1	Step Shaft	50

7.2	Shaft02	51

8	Additional Tasks Milling	52

8.1	Flange	52

8.2	Exercise11	53

# Preface

This training document 'Fundamentals of CNC Programming’ is the prerequisite for working with the additional modules with SINUTRAIN.

Today, CNC controllers are considered the most essential part of any automation. Depending on the problem definition, the most varied tasks in the areas of turning, milling, lasering, and grinding as well as in many other areas can be carried out economically with the controllers ShopMill and ShopTurn.

.

Training objective:

The CNC S01module is structured in a way that you have before you a completely programmed workpiece in G-code programming (DIN 66025).

The same workpiece is generated step by step with this document according to the machining step programming. In this way, you will learn the simple operation of this software, and control and optimize it with the simulation.

Required Hardware and Software

1	PC, operating system Windows XP Professional starting with SP1 with 500 MHz and 256 MB RAM, free disk storage approx.  400 MB, of that 50 MB on the system drive, 1GB for installing all products, MS Internet Explorer starting with 6.0

2     Software SINUTRAIN 802D/ 810D/840D/840Di/Programming &Training, SinuTrain/JopShop

# Introduction

## Development Phases of CNC Technology

- At the beginning of the eighties, first CNC machines with simple controllers

- In the middle of the eighties, more powerful controllers with cycles because of faster processors

as well as machine tools with greater processing speed

- At the end of the eighties, machine tools with 5 and more axes and special software tools

for external programming by using CAD/CAM systems

- At the beginning of the nineties,  flexible  manufacturing systems with extensive supplementary functions 	  such as palette systems and multiple clamping with multiple spindle drives

- In the middle of the nineties,  continued development of tool systems and the use of special tools for	  	   processing  complex workpiece contours with only one tool

- End of the nineties: central programming systems for programming several different controllers at different 	   machine tools

## Controller Requirements for the New Millennium

- Openness: It is to be possible for the machine manufacturer or the user to configure and expand controllers 	  according to their own requirements

- Independence: Programming by means of a uniform controller interface for the most varied CNC processing

- Equality:  All machine data is to be available also at the external programming units.

Programming at the external programming units is the same as on the machine tool. 	 	 	- Saving programming time:  With graphic machining plans and help displays, it is to be possible to 	  	  generate complex workpiece contours very easily and quickly

- Editing capability: Extensive editing functions provide for fast and simple program changes/program 	 	  expansion

## Advantages of CNC Programming with SinuTrain SHOPMILL, SHOPTURN

The controller is continuously optimized and can be adapted any time to the individual requirements of the machine manufacturers.  Moreover, cycles and functions can be integrated later.

Regardless of whether turning, milling, or any other type of processing is performed, always the same program interface and the same menus or functions are used.

Retrofit: This means: Siemens can retrofit also older CNC machines to ShopMill and ShopTurn.

Advantage:  Operating the software and the menu structure has to be learned only once.

By transferring the machine data to the programming system of  SINUTRAIN, programming at the external programming unit is the same as on the machine tool.

By using contour calculators and CAD readers, simple programming is possible without technical terms. By directly entering technological values, no external calculations have to be made beforehand. The integrated contour calculator is able to process all conceivable dimensions, yet is very simple to handle.  Through work step programming and many online help functions, extensive programming tasks can be solved very quickly.

Convenient programming is possible with functions such as Copy, Cut, and Insert. Since the program is generated in the editor as a graphic machining plan by means of individual work steps, all editing steps are provided in a straightforward arrangement.

# Programming a Turned Part in G-Code

# Programming a Turned Part according to the Machining Step Procedure

Using this drawing, we will generate a program in the machining step procedure.

## Starting SINUTRAIN

To start SinuTrain, double click on  ,

or start SinuTrain using the start bar.

## Selecting the Machine

After booting up the computer, a menu is displayed with a selection of machines with the respective version number.

1. Select turning machine with >> ShopTurn Open V 06.04 <<

2. Click the Start button

## SINUTRAIN Basic Display

After selecting the machine, the basic display of SINUTRAIN appears.

From here, all SINUTRAIN actions are started.

## Generating the Turning Program

## Setting Up a New Directory/Program Generation

Various actions can be performed in the Program Manager

(for example: New, Rename, Copy, etc.)

By pressing the softkeys  	  , the available directories are opened in the operating area DIRECTORY <<VERZEICHNIS>> under ShopTurn.

With the softkey  , we are now setting up a new directory with the name "Work pieces“ <<Werkstuecke>>.

Confirm the input with OK.

The directory with the name “Work pieces“ is set up.

By pressing the arrow key    on the CNC keyboard or with the cursor key toward the right, the selected directory opens.

Note

The cursor keys can be used for navigating in SinuTrain.

## Setting Up a New Workpiece Program

After the directory is opened, existing programs are displayed, or new programs can be set up.

By pressing the softkey  and the selection Shopturn or G-Code (vertical softkeys), a new program name “Name of the machining plan“ is entered,

in our case  “Shaft“ <<“Welle“>>.

Confirm input with OK.

## Program Header

The program header of the new program opens automatically. In the program header, the following is entered: the workpiece data, zero shift, raw part pattern, distance to the chuck, retraction planes, tool change point, safety clearance incremental or absolute, and the spindle speed limitation.

.

With the softkey  you can now call the associated help display.

Make all inputs as indicated in the display above

and accept  the input into the machining plan.

Note

With the softkey  you can alternate, for example, between different zero points, units of mass, mm, inch, raw part shapes, cylinder, pipe, rectangle, corner,  etc.

The blue line above always shows you the current input type.

## Program Editor

Entered/edited in the program editor in the form of machining steps.

## Tool Selection

First, you need a tool for face turning and for roughing the outside contour.

Click on

Then, by clicking on “Tools“ again, call the tool list.  Here, the tools that have already been set up are provided. But you can also create new ones.

Accept the roughing tool. The finishing tool and the threading tool are added later from the tool list.  The grooving tool has to be set up, however.

Click on    	ROUGHING TOOL

Now, enter the data for the constant cutting speed and the plane.

Accept the values with the input key.

If needed, change the unit or selection with

and finally confirm your input with

The roughing tool is included in the program, with all the data.

## Face Turning

Positioning for face turning in rapid feed.

By using line/circle, we can program a travel movement.

Click on .  Enter X80 Z0.1 and click on

Confirm with

Next, face the front of the workpiece to X-1.6 (2 x plate radius size R=0.8)

so no residual material remains in the center.

Click on   and enter X-1.6 and F0.3 and  mm/U

Confirm with

Now, position on X90 Z5 at rapid feed.

After accepting, you are back in the program.

## Workpiece Contour

The contour is generated with the contour calculator.

Click on the button    below and then in the upper right on

Assign a name to the new contour; then the contour calculator opens.

The first input specifies the starting point.

EnterX0 Z0 and confirm with

Note

With the buttons  we describe the contour.

Here, the first diameter of the finished part contour is described.

A chamfer 2 x 45 degrees as transition element is appended to the end of the element.

Click on the button   and enter X30 and FS 2.

Click on the button    and enter Z-20.

Click on the button    and enter X40    R2.5.

Click on the button    and enter X50 Z-30.

Click on the button    and enter Z-44    R2.5.

Click on the button   and enter X60  FS1.

Click on the button   and enter Z-70 and R1.

Click on the button   and enter X66 and R1.

Click on the button   and enter Z-77 and R1.

Click on the button   and enter X82 and FS3.

The raw part is diameter 80 in the program and is run to 82, in order to gain distance from the tool. For 	       that reason, the chamfer size has to be programmed 1mm larger.

The finished part contour has now been described, and is accepted into the program with .

After that, you are back in the program editor.

## Stock Removal Cycle Roughing

The stock removal of a contour is performed in the area Contouring and Stock Removal.

Using the “Help Key“ brings up the help display.

Click on the button    and  .

Select the tool and enter the cutting data.

Accept all other data in the picture.

Here, you should test the program with a simulation display.

Click on the button

Clicking on the button "End“ takes you back to the program editor.

## Finishing the Outside Contour

The outside contour is executed with the finishing tool contour parallel.

Click on the button   and

Select the tool and enter the cutting data.

Accept all other data from the figure.

## Thread Undercut

We incorporate the undercut DIN 76

Click on the button    and    and then on

Use all data from the figure and exit the menu with  .

We can see here that the contour during roughing and finishing is connected with stock removal. The thread undercut was generated with its own cycle.

Here, you can test your program with the simulation display.

## Thread Cutting

A thread of M30 X 1.5 is to be manufactured.

Click on   and on    and enter the values.

## Making Grooves

Finally, we are making two grooves.

Click on    and on    and enter the values.

Exit menu with  .

We are done with our machining step program.

## Simulation

Finally, test your program with a simulation display.

First in the side view.

Next in the 3 window view

and in the volume model.

Using EXIT, we exit the ShopTurn software.

# Programming a Milled Part in G-Code

PLANFRAESER = facing tool

FRAESER = milling tool

ZENTRIERER = centering tool

# Programming a Milled Part according to the Machining Step Process

## Start SINUTRAIN

To start SinuTrain, double click on

or start SinuTrain using the start bar.

## Selecting the Machine

After you booted the computer, a menu is displayed with the selection of machines with the respective version number.

1. Select milling machine  >> ShopMill Open V 06.04 <<.

2. Click on the Start button.

## SINUTRAIN Basic Display

After you selected the machine, the basic display of SINUTRAIN appears.

All SINUTRAIN actions are started from here.

## Setting Up a New Directory/Program Generation

Different actions can be performed in the program manager.

By clicking on the softkeys 	 , the available directories are opened under ShopMill, in the operating area DIRECTORY

With the softkey   we are now setting up a new directory called

"Pattern plate“.

Confirm the input with OK.

The selected directory opens by pressing the arrow key    on the CNC keyboard, or with the cursor key toward the right.

## Setting Up a New Workpiece Program

After opening the directory, existing programs are displayed, or new programs can be set up.

By pressing the softkey    and selecting ShopMill or G-Code (vertical softkeys),  a new program name “Name of the work plan“ is entered; in our case “Pattern plate“.

Confirm the input with OK.

## Program Header

The program header of the new program opens automatically. The following is entered in the program header: the workpiece data, zero shift,  raw part pattern, distance to the chuck, retraction planes, tool change point, safety clearance incremental or absolute, and the spindle speed limitation.

With the softkey    you can now call the associated help display.

Enter all data as in the figure above

and accept the inputs in the machining plan with  .

Note

With the softkey   you can alternate, for example, between different zero points and measurement units, mm, inch. The blue line above always shows the current input type.

## Outside Contour

The contour is generated with the contour calculator.

Click on the button    below and then in the upper right on   .

Assign a name to the new contour; after that, the contour calculator opens.

The first input specifies the starting point.

Complete programming the outside contour with the contour calculator.

The outside contour is now described, and is accepted into the program with .

## Roughing the Outside Contour

To perform the machining step roughing on the outside, with contour compensation on the left, do the 	       following:

Click on    and on   and enter the values.

## Selecting the Tool

Here the tools that have already been set up are provided. But you can also generate new ones.

Here, take the MillingTool32.

Click on   to accept the selected tool.

Accept all data from the graphic and exit the menu with  .

## Finishing the Outside Contour

To perform the machining step Finishing Outside, with contour compensation to the left, do the 	  	       following:

Click on    and enter the values.

Accept all values from the figure, and exit the menu with  .

Here, you can test your program with the simulation display.

## Stock Removal, Residual Material and Finishing of Contour Pockets and Inside Contour

The contour is generated with the contour calculator.

Below, click on the button    and then in the upper right on   .

Assign a name to the new contour; then the contour calculator opens.

The first input specifies the starting point.

With the contour calculator, complete programming the inside contour.

The inside contour is now described and is accepted into the program with .

## Stock Removal of Contour Pocket Roughing

Click on    and on   and enter the values.

Select the tool and enter the cutting data.

Accept all additional data from the figure.

## Removing Residual Material from the Corners

Click on  and on   and enter the values.

Select the tool and enter the cutting data.

Accept all additional data from the figure.

## Finishing the Base

Click on   and on   and enter the values.

Select the tool and enter the cutting data.

Accept all additional data from the picture.

## Finishing the Edge

Click on    and on   and enter the values.

Select the tool and enter the cutting data.

Accept all additional data from the picture.

.

## Roughing the Circular Pocket Diameter 60

Click on    and on   and enter the values.

Select the tool and enter the cutting data.

Accept all additional data from the picture.

## Finishing the Circular Pocket Diameter 60

Click on    and on  and enter the values.

Select the tool and enter the cutting data.

Accept all additional data from the picture.

## Roughing the Circular Pocket Diameter 30

Rough the circular pocket yourself.

Important: The starting depth is no longer at “0“ but at “-10mm“

## Finishing the Circular Pocket Diameter 30

Rough the circular pocket yourself.

Important: The starting depth is no longer at “0“ but at “-10mm“

## Centering and Drilling taking Obstructions into Account

For centering and drilling, first the corresponding machining steps are programmed, and then the individual positions are specified.

The obstructions have to be taken into account when positioning.

## Machining Step Centering

Click on    and on   and enter the values.

Select the tool and enter the cutting data.

Accept all additional data from the picture.

## Machining Step Drilling

Click on    and on  and enter the values.

Select the correct tool for drilling, enter the cutting data

and exit the menu with

## Inputting the Line of Holes to the Left

Click on          and enter the values for the

“left“ side.

## First Obstruction

Click on   and enter the Z value.

## Inputting the Line of Holes to the Right

Click on           and enter the values for the

“right“ side.

## Second Obstruction

Click on    and enter the Z value.

## Drilling the Full Circle

Click on           and enter the values for the

right hole circle.

## Third Obstruction

Click on    and enter the Z value.

## Drilling a Single Hole

Click on          and enter the values.

## Simulation

Finally, test your program by using the different simulation displays.

# Additional Tasks for Turning

## Step Shaft

## Shaft02

# Additional Tasks Milling

## Flange

## Exercise11

# Text boxes

Additional
CNC Programming with mit ShopMill

2 to 3 days Modules S03

Additional  
CNC Programming with ShopTurn

2 to 3 days Modules S02

2. SINUTRAIN

Fundamentals of
CNC Programming with SINUTRAIN

2 to 3 days   Modules S01

Schrupper =  roughing tool

Schlichter = finishing tool

Gewindestahl = threading tool

Stecher = grooving tool

All non-dimensioned radii

1 PC