Training Manual for Integrated Automation Solutions

Totally Integrated Automation (TIA)

MODULE E11

Radio Frequency Identification (RFID)

with SIMATIC S7-300F-2 PN/DP and RF180C

This manual was prepared for training purposes by Siemens AG for the project Siemens Automation Cooperates with Education (SCE).

Siemens AG does not guarantee the contents of this document.

Passing on this document as well as copying it, using and communicating its contents is permitted within public training and continued education facilities.  Exceptions require the written permission by Siemens AG (Michael Knust michael.knust@siemens.com).

Violators are held liable to pay damages. All rights -including translation- reserved, particularly if a patent is granted, or a utility model or design is registered.

We wish to thank the Michael Dziallas Engineering corporation and the instructors of vocational schools as well as all those who provided support during the preparation of this manual.

PAGE

1	PREFACE	5

2	Notes regarding the usage of CPU 315F-2 PN/DP	7

3	Notes regarding the SIMATIC RFID components	8

4	RFID Fundamentals	9

5	Starting up an RFID project with CPU 315F-2 PN/DP and RF180C	10

5.1	Setting Up a New Project	11

5.2	Configuring the Hardware	13

5.3	Assigning a Device Name	20

5.4	Inserting UDT Blocks and FB45	22

5.5	Generating Data Blocks	23

5.6	Programming a Restart or Warm Restart	32

5.7	FC11 Function for a Command or Request	33

5.8	Basics of Entries at Command Block FC11	35

5.9	Command String	38

5.10	Basics of FB45 and DB45	39

5.11	FB10 Reader_Control Program	48

5.12	FB1 Control Program	51

5.13	OB1 Program Call	56

5.14	Variable Table STATUS_SLG_1	57

5.15	Variable Table STATUS_SLG_2	58

5.16	Symbol Table	59

5.17	Block Folder	60

5.18	DB49 Data View	60

The following symbols serve as a guide through this module:

Information

Programming

Sample Task

Notes

# PREFACE

Regarding its content, Module E11 is part of the instruction unit 'IT Communication with SIMATIC S7’.

Objective

In Module E11, the reader will learn how networking and data exchange between PLCs and RFID components is set up.

As PLC, the CPU 315F-2 PN/DP and as Radio Frequency Identification (RFID), a SIMATIC RFID system is used. The RFID components consist of the interface module RF180C (ASM) with write/read device RF310R (Reader or SLG (write/read device)) and different mobile data systems such as RF340T, RF350T, RF360T or ISO Moby D MDS D124 (transponder or MDS). PROFINET is used for networking the PLC and the SIMATIC RF180C.

Module E11 shows in principle the procedure for the startup, based on a brief example.

Prerequisites

To successfully work through Module E11, the following knowledge is assumed:

(	How to handle Windows

(	Fundamentals of PLC programming with STEP7 (for example, Module A ‘Startup’ PLC 	Programming with STEP7).

(	Fundamentals of network engineering (for example, Appendix V – Basics of Network 	Engineering)

Hardware and Software Required

1	PC, operating system Windows XP Professional with SP2 or SP3/Vista 32 bit Ultimate and Business/Server 2003 SP2 with 600MHz (only XP)/1 GHz and 512MB (only XP)/1 GB RAM, free disk storage approx.  650 to 900 MB, MS Internet Explorer 6.0 and network card

- Software STEP 7 V 5.4

- PLC SIMATIC S7-300 with CPU 315F-2 PN/DP and at least one digital Input and output module

Sample configuration:

- Power supply: PS 307 2A

- CPU: CPU 315F-2 PN/DP

- Digital inputs: DI 16x24V DC

- Digital outputs: DO 16x24V DC/0.5 A

- SIMATIC RF180C IM (interface module)

RF310R or RF340R SLG (write/read device)

Different transponder MDSs (Mobile Data System)

of the type:

RF340T (8 KB)

RF350T (32 KB)

RF360T (64 KB)

ISO Moby D MDS D124 (112 bytes)

- Ethernet connection between PC, CPU 315F-2 PN/DP and RF180C

# notes regarding the usage of CPU 315F-2 PN/DP

The CPU 315F-2 PN/DP is a CPU that is shipped with 2 integrated interfaces.

- The first interface is a combined MPI/PROFIBUS DP interface that can be used at the

PROFIBUS DP as master or slave to connect distributed IO/field devices with very fast reaction time.

In addition, it is possible to program the CPU here by means of an MPI or PROFIBUS DP

- The second interface is an integrated PROFINET interface.

This allows for using the CPU as PROFINET IO controller to operate distributed IO

on PROFINET. The CPU can be programmed by means of this interface also!

- Moreover, it is possible to use fail-safe IO devices on both interfaces.

Notes:

-	In module E11, the CPU 315F-2 PN/DP is used as the controller for the data exchange of a  	SIMATIC RFID system on the PROFINET.

-	To run this CPU, a micro-memory card is required!

- The addresses of the input and output modules can be parameterized at this CPU.

# notes regarding the SIMATIC RFID components

The communication module RF180C is a module for operating RFID components at any controller by means of PROFINET IO.

At the RF180C, up to 2 readers (SLG = write/read device) can be operated in parallel. The user can start a command in parallel on two readers (FB 45 if operated on a SIMATIC S7)

The tag data is accessed by means of addressing the tag physically.

In the SIMATIC S7, FB 45 is provided for this. FB 45 makes available to the S7user an interface that is easy to handle and is equipped with powerful commands (processing a complete tag with a single command; command chaining; S7 data structures by means of UDTs).

The RF180C is integrated into the hardware configuration by means of a GSDML file.

Then, the RF180C can be configured by means of  HWConfig of the SIMATIC Manager.

The GSDML file is provided on the CD "RFID Systems“.

Additional information is available in the operating instructions

"RFID Systems Communication Module RF180C“.

# RFID fundamentals

Radio Frequency Identification (RFID) makes it possible to automatically identify and localize  objects and living beings, and thus considerably facilitates recording and storing data. The RFID system consists of  the following: 1) a transponder that is located in the object or in the living being and identifies it, and 2) a reading device for reading out the transponder ID. The reading device includes a software (a micro-program) that controls the actual read process, and an RFID middleware with interfaces to other EDP systems and data bases.

As a rule, a read device generates an electro-magnetic high frequency field with a short range, preferably with induction coils.  It is not only used to transmit data, but to also to supply the transponder with power. Only if larger ranges are to be obtained are active transponders used that have their own power supply. Usually, the frequency of 13.56 MHz is used (RF300, ISO). The reading device (reader) generates a high frequency electromagnetic alternating field that illuminates the aerial of the RFID transponder (RFID tag).  As soon as the aerial coil enters the electro-magnetic field, an induction current is generated in it. This current is rectified, and with it, a capacitor is loaded as short time storage which, for the read process, provides for the power supply of the chip. For active tags, an installed battery takes care of the supply. The micro-chip thus activated in the RFID tag decodes the commands sent by the reader. This reader encodes and modulates the reply into the irradiated electro-magnetic field through field weakening in the contact-free short circuit, or in opposition reflection of the field that the reader transmitted.  With this, the tag transmits its own unchangeable serial number, additional numbers of the marked object, or other data that the reader polled.  The transponder itself does not transmit a field; it only changes the reader’s electro-magnetic transmission field.

Transponder switch open, aerial is on "Absorption“ (return value 0).

Transponder switch closed, aerial is on "Reflect“,  (return value 1).

(Source: Wikipedia)

# starting up an RFID project with CPU 315F-2 PN/DP and RF180C

Below, the startup of an RFID project is described.

As SIMATIC S7-300 station, the CPU 315F-2 PN/DP is used.

In the CPU’s control program, a data structure has to be generated -by means of a function block call (FB45)-  with data blocks and embedded UDT data types.

In our example, it has to be possible to perform the following actions for each reader:

- Writing data to the transponder (DB48 of the CPU to the MDS).

- Reading the data from the transponder (MDS to DB48 of the CPU).

- Reading the transponder data information (MDS to DB49 of the CPU).

- Reading the reader status information (reader to DB50 of CPU).

The data structure of the German language UDTs is as follows:

To generate the data structure, the required UDT data types have to be imported to the

Step 7 project and function block FB45.

A sample program with the blocks is provided on the CD "RFID Systems“.

Additional information about the data structure is available in the function manual

"RFID Systems FB45“

## Setting Up a New Project

1. 	The central tool in STEP 7 is the ’SIMATIC Manager’, which we call here with a double click.       (® SIMATIC Manager)

2. 	STEP 7 programs are managed in projects. We are now setting up such a project

(® File ® New)

3.	Next, we are assigning the ’Name’ 'RFID_RF180C’ to the project (® RFID_RF180C ® OK)

- Highlight your project and insert an ’Industrial Ethernet Subnet’

(( RFID_RF180C ( Insert ( Subnet ( Industrial Ethernet).

- Then, we insert a ’SIMATIC 300 Station’. (® Insert ® Station ® SIMATIC 300 Station)

## Configuring the Hardware

- With a double click, open the configuration tool for the ’Hardware’. (® Hardware)

- Open the hardware catalog by clicking on the symbol '’. (® )

Insert the ’Mounting channel’ with a double click (® SIMATIC 300 ® RACK 300

® Mounting channel).

Note

A configuration table for configuring Rack 0 is displayed automatically.

- From the hardware catalog, we can now select all modules that are present in the actual rack and insert them in the configuration table. To this end, we click on the name of the respective module, hold the mouse key and drag it to a line in the configuration table.

We start with the power unit ’PS 307 5A’ (® SIMATIC 300 ®  PS-300 ® PS 307 5A).

Note

If your hardware deviates from the one displayed here, simply select the corresponding modules from the catalog and insert them in your rack. The order numbers for the individual modules -that are also inscribed on the modules- are displayed in the footer of the catalog.

- Next, we drag the ’CPU 315F-2 PN/DP’ to the second slot.

The order number and the version of the CPU are inscribed on the front of the CPU.

(® SIMATIC 300 ®  CPU-300 ® CPU 315F-2 PN/DP ® 6ES7 315-2FH13-0AB0 ® V2.6)

- When entering the CPU, the following window appears.  In this window, we do the following: assign to CPU 315F-2 PN/DP an ’IP- address’, specify the ’Subnet screen form’ and select the ’Ethernet’ that has already been set up.  Optionally, a ’Router address’ can be selected for network-overarching communication. Confirm your entries with ’OK’ (( IP address: 192.168.0.100 ( subnet screen form: 255.255.255.0 ( Ethernet(1) ( Don’t use a router ( OK)

Notes regarding networking on the Ethernet (additional information is provided in Appendix V of the training manual):

MAC address:

The MAC address consists of a permanent and a variable part. The permanent part ("Basic MAC address") identifies the manufacturer (Siemens, 3COM, ...). The variable part of the MAC address differentiates the different Ethernet stations and should be assigned globally unique. On each module, a MAC address specified by the factory is inscribed.

Value range for the IP address:

The IP address consists of 4 decimal numbers in the value range 0 to 255, separated by a period; for example: 141.80.0.16

Value range for the subnet screen form:

This screen form is used to establish whether a station or its IP address belongs to the local subnet, or can be reached only by means of a router.

The subnet screen form consists of 4 decimal numbers in the value range 0 to 255, separated by a period; for example:  255.255.0.0

The 4 decimal numbers of the subnet screen form have to contain  -in their binary representation- from the left a series of gapless values "1" and from the right a series of gapless values "0"..

The values "1" determine the area of the IP address for the network number. The values "0" determine the area of the IP address for the station address.

Example:

Correct values:	255.255.0.0 Decimal = 1111 1111.1111 1111.0000 0000.0000 0000 binary

255.255.128.0 Decimal = 1111 1111.1111 1111.1000 0000.0000 0000 binary

255.254.0.0 Decimal = 1111 1111.1111 1110.0000 0000.0000.0000 binary

Incorrect value:	255.255.1.0 Decimal = 1111 1111.1111 1111.0000 0001.0000 0000 binary

Value range for the address of the gateway (router):

The address consists of 4 decimal numbers in the value range 0 to 255 separated by a period; for example, 141.80.0.1.

Relationship of the IP addresses, router address and subnet screen form:

The IP address and the gateway address must differ only at those positions where an "0" is shown in the subnet screen form.

Example:

You entered the following: for subnet screen form 255.255.255.0; for IP address 141.30.0.5 and for router address 141.30.128.1.

The value for the IP address and the gateway address is to differ only in the 4th decimal number. However, in the example, the 3rd position already differs.

In the example, we have to alternatively change:

- the subnet screen form to: 255.255.0.0 or

- the IP address to: 141.30.128.5 or

- the gateway address to: 141.30.0.1

- Next, we are dragging the input module for 16 inputs to the 4th slot.  The module’s order number is located on the front. (® SIMATIC 300 ® DI-300 ® SM 321 DI16x24VDC).

Note

Slot 3 is reserved for interface modules and remains empty for that reason.  The module’s order number is indicated in the footer of the catalog.

- Now we drag the output module for 16 outputs to the 5th slot. The module’s order number is located on the front (® SIMATIC-300 ® DO-300 ( SM 322 DO16x24VDC/0.5A).

Note

The module’s order number is indicated in the footer of the catalog.

- Now, we have to change the PROFINET device name to PN IOx100.

Select ’PN-IO’ with a double click. (® PN-IO,( PN-IOx100,( OK)

- Now, drag the PROFINET IO System (100) module tier toward the right and from the folder  PROFINET IO, insert the SIMATIC RFID module RF180C into the module tier by dragging it there.

If module RF180C should not yet be selectable, it first has to be inserted by a data carrier, using the menu "Options“ Install GSD files.

- Then, double click on the inserted module and change the device name to RF180Cx110 and the IP address to 192.168.0.110

- By clicking on '’, the hardware configuration is saved and compiled.

## Assigning a Device Name

- First, highlight the module RF180C and then select, under the menu "Destination system“ and under Ethernet Assign device name.

Note

A prerequisite for this is that the die PG/PC interface is set to TCP/IP and the PC’s network card is configured correctly.  For example, IP address 192.168.0.99, subnet 255.255.255.0 and router address -.-.-.- (refer to Module E02)

18.  Highlight the SIMATIC RFID module and then click on the button “Assign name“. Then close the window.

This is what the completed hardware configuration with the associated addresses looks like

- By clicking on '’ we can load the hardware configuration to the PLC. The operating mode switch on the CPU should be on Stop ( ®  ).

- Close hardware configuration.

## Inserting UDT Blocks and FB45

De-archive the library "RFID_FB45_UDT_Blocks“ from the template directory and open it.

Copy UDT11, UDT21, UDT 111, UDT261, UDT271, UDT281 and FB45 and insert them in the block folder.

Close the library.

Note

Instead of the library RFID_FB45_UDT_Blocks, the sample program MOBY FB45 can be de-archived. The file FB45_V1_3.zip is available on the RFID Systems CD in the directory "Data“, sub-directory "FB45“.

## Generating Data Blocks

DB48 Write/Read Data

Here, the source data of a write request to the transponder is stored, or the destination data for the read request from the transponder.

Generating DB48

Open DB48, set up 1024 bytes

Under Name, enter “Data“.

At Type Combined data, select (with the right mouse key) the ARRAY data format.

Enter 1..1024 within the brackets.

In the next line, select or enter BYTE.

Save and close DB48

DB49 MDS Status Information

In DB49, the MDS status Information is entered.

The information is stored in a data block with a specified structure.

Read MDS status with Sub_Command 01according to UDT261 or Sub_Command 02 according to UDT271.

Generating DB49

Open DB49 and insert UDT261 and UDT271

DB49 data view

The start address in DB49 is “0“ for Sub_Command 01 and “18“ for Sub_Command 02.

The data length is 18 bytes in both cases

Save and close DB49

DB50 Reader Status Information

The reader status information is entered in DB50.

Depending on the request, the information has to be stored in a data block with a specified data structure.

Read reader status with Sub_Command 01 according to UDT111 or Sub_Command 06 according to UDT281.

Generating DB50

Open DB50 and insert UDT111 and UDT281

Open DB50 and insert UDT111 for Reader_Status.

For Reader_diagnosis, insert UDT281.

Data view of the Reader status in DB50 (UDT111) Byte 0 to 27

Data view of the Reader diagnosis in DB50 (UDT281) Byte 28 to 55

For Sub_Command 01, the start address in DB50 is "0“ Reader status information and

for Sub_Command 06 "28“ Reader diagnosis information.

The data length in both cases is 28 bytes.

Save and close DB50

DB47 Request Data Block

The DB47 is set by means of the UDT11 in DB45.

In DB47, a UDT21 is embedded for each reader.

The request commands are then entered in the respective UDT21.

The data of the read/write request is then stored in DB48.

The reference to DB48 is assigned in UDT21 of DB47.

Generate DB47

Open DB47 and add UDT21 for each request

Open DB47 and for Reader1, insert the UDT21 five times by means of ARRAY format.

For Reader2, also insert UDT21 five times by means of ARRAY format.

Note

In our example, five request commands are possible for each reader or channel.

Thus, the UDT21 is embedded in DB47 10 times.

The commands or requests of the second reader start with address 50.

Data View of DB47

(Starting with byte 50, the commands for Reader2 or channel 2 start)

Save and close DB47

DB45 Reader Parameter Block

Each MOBY channel (reader) needs its own parameters. These are predefined in a data structure as UDT 10 (with English comments), UDT 11 (with German comments) and UDT 14 (with Spanish comments). This UDT has to be called for each MOBY channel in a data block. In UDT 11, different variables are defined:

• INPUT parameters: The user has to enter these variables once during configuration (exception: command_DB_number/command_DB_address). It is not necessary to change or poll these parameters during the entire execution time.

Please note that when an INPUT parameter is changed, an init_run has to be performed before the new setting takes effect (refer to chapter "Programming Restarts and Warm Restarts").

• Control bits: With these Boolean variables, the user starts his commands.

• Displays: The displays show the user the progress of his commands. Errors are easy to analyze.

• Internal FB variables: These variables are of no significance to the user. They must not be changed by the application. Otherwise, malfunction and data corruptions would be the result.

Generating DB45

Open DB45 and insert UDT11 for each reader

In DB45, UDT11 is called for each reader

Entries in DB45

The base address for the RF180C is 256 (refer to hardware), here to be entered at address 0.0 and 50.0

The selection of Reader1 has to be entered under address 2.0.

The selection of Reader2 has to be entered under address 52.0.

DB47 (request data block) is referred to in DB45.

The requests of the first reader have to be entered in DB47 starting with DBB0, here at address 4.0 and 6.0

The requests of the second reader have to be entered in DB47 starting with DBB50, here at address 54.0 and 56.0.

No other values are changed.

For the entries in DB45, take note that the DBs continue to be chained correctly.

Data view of DB45 to byte 33:

Data view of DB45 starting with byte 34 (SLG = Reader)

Save and close DB45

Note

The inputs in the data block are entered as actual value.

Take note that when the data block is initialized or a general reset is performed on the CPU, the actual values are overwritten with the start values of the data blocks.

Additional information about setting up the data structure with data blocks and about the individual UDTs is provided in the function manual "RFID Systems FB45“.

## Programming a Restart or Warm Restart

A restart of the MOBYIM (interface module) is carried out by setting the variable "init_run".

With "init_run“, the IM and FB45 are re-parameterized and synchronized.

"init_run“ is necessary after the following:

• Switching on the SIMATIC (OB 100)

• Switching on the power supply for the IM

• PROFINET communication is interrupted

• An error indication by the variable "error_BUS"

• A transponder type change; for example from RF300 to ISO or vice versa

• Changing an INPUT parameter in DB45 (Reader_Parameter)

Generating OB100

Open OB100 and enter the program

Save and close OB100

## FC11 Function for a Command or Request

Before starting a MOBY command with "command_start“, we have to define it. For a simple definition of a command, UDT 21 (German comments) is provided. UDT21 is embedded in DB47 multiple times.

So that not all inputs have to be carried out in DB47, here a block for one command or request is generated.

It is then possible to call this block in the control program multiple times; for example for a command string.

Generating Function FC11

Set up a new FC11 function.

Set up IN variables

Set up OUT variables

Enter Networks 1 to 6

Save and close FC11

## Basics of Entries at Command Block FC11

The values for DB47 are specified by means of the input variables of FC11.

One UDT21 is used for each request or command.

Data View of the UDT21

Command Overview

| Command (hex) | Command |
| --- | --- |
| Normal | Chained* |  |
| 01 | 41 | Write data to MDS |
| 02 | 42 | Read data from MDS |
| 03 | 43 | Initialize MDS |
| 04 | 44 | Reader status |
| 06 | -- | NEXT |
| 08 | 48 | END; end communication with the MDS |
| 0A | 4A | Aerial on/off |
| 0B | 4B | MDS status |
| *) Not all readers or IM modules support chained commands. Note the information in the MOBY manuals for configuration, installation and service. |

Writing data to the transponder

| Command (hex) | Sub_command | length [dec] | address_MDS [hex] | DAT_DB [dec] | Comment |
| --- | --- | --- | --- | --- | --- |
| 01 | - | 1 to 32767 * Length of the MSD data to be written | 0000 to FFFF Starting with this start address, the data is written to the MDS | Pointer to the user data that is to be written to the MDS |  |

Reading data from the transponder

| Command (hex) | Sub_command | length [dec] | address_MDS [hex] | DAT_DB [dec] | Comment |
| --- | --- | --- | --- | --- | --- |
| 02 | - | 1 to 32767 * Length of the MSD data to be read | 0000 to FFFF Starting with this start address, the data is read from the MDS | Pointer to the user data. Here, FB45 stores the MDS data that was read. |  |

Initialize Transponder

| Command (hex) | Sub_command | length [dec] | address_MDS [hex] | DAT_DB [dec] | Comment |
| --- | --- | --- | --- | --- | --- |
| 03 | 00 to FF hex value that is written to the MDS | - | Memory size of the MDS to be initialized | - |  |

Read out Reader status

| Command (hex) | Sub_command | length [dec] | address_MDS [hex] | DAT_DB [dec] | Comment |
| --- | --- | --- | --- | --- | --- |
| 04 | 01 = status according to UDT 110¹ 02 = status according to UDT 120¹ (last commands) 03 = status according to UDT 130¹ (error indications) 04 = status according to UDT 140¹ (MDS in the field) 05 = status according to UDT 150 (communication quality) 06 = status according to UDT 280 (diagnosis data) |  |  | Pointer to the result. The result is represented with the corresponding UDT (refer to sub_command) | MOBY U/D or RF300 MOBY U MOBY U MOBY U RF300 |

(In our example, we are using the German language UDT111 and UDT281 for RF300)

Command NEXT

| Command (hex) | Sub_command | length [dec] | address_MDS [hex] | DAT_DB [dec] | Comment |
| --- | --- | --- | --- | --- | --- |
| 06 | - | - | - | - | NEXT: processing this MDS is completed |

Command END

| Command (hex) | Sub_command | length [dec] | address_MDS [hex] | DAT_DB [dec] | Comment |
| --- | --- | --- | --- | --- | --- |
| 08 | 00 = Processing with the MDS is ended 01 = Processing pause with the MDS¹ | - | - | - | ANZ_MDS_present is reset ANZ_MDS_present remains set |

Switching the reader aerial on/off

| Command (hex) | Sub_command | length [dec] | address_MDS [hex] | DAT_DB [dec] | Comment |
| --- | --- | --- | --- | --- | --- |
| 0A | 01 = switch on aerial 02 = standby: Switch aerial off 09 = adjust aerial to the environment (FFT) | - | - | - | The command Aerial on/off can not be started with command repetition (refer to chapter "Command Repetition) Only Reader 80 (MOBY F) |

Transponder Status

| Command (hex) | Sub_command | length [dec] | address_MDS [hex] | DAT_DB [dec] | Comment |
| --- | --- | --- | --- | --- | --- |
| 0B | 00 = status and diagnosis | - | Today’s date (week/year) to calculate the life of the battery (for example, 1401 hex = 20th week of year 2001) | Pointer to result. The result is represented with UDT 100 | only MOBY U (refer to chapter "The UDTs of FB45“) |
|  | 01 = type and write protection status | - | - | Pointer to result. The result is represented with UDT 260 | RF 300 (refer to chapter "The UDTs of FB45“) |
|  | 02 = diagnosis data | - | - | Pointer to result. The result is represented with UDT 270 | RF 300 (refer to chapter "The UDTs of FB45”) |

(In our example, we are using the German language UDT261 and UDT271 for RF300)

Notes

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

## Command String

The user configures the command string by storing a corresponding number of UDT 21 one after the other in a DB. All commands that are strung together have to be of the "Command" type "4x". The last command of a string has to be of the type 0x. With it, the FB 45 recognizes the end of a command string.

Example of a command string in DB47

Four data records are to be processed by an MDS.

The command structure is stored in the request DB, as shown below.

The destination and source data of the MDS are stored consecutively in DB48.

Read MDS address 0000 hex length 600

Read MDS address 1000 hex length 100

Read MDS address 1200 hex length 1

Write MDS address 1200 hex length 1

Notes

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

## Basics of FB45 and DB45

FB45 accesses DB45. In DB45, a UDT11 is embedded for each reader.

Data view of the UDT11

Input Parameters of the UDT11

The user has to enter these variables during configuration (exception: command_DB_number/ command_DB_address).

It is not necessary to change or poll these parameters during the entire execution time.

Please note that before the new setting takes effect,  "init_run“ has to be performed after an INPUT parameter is changed (refer to chapter "Programming Restarts and Warm Restarts").

| Variable | Description |
| --- | --- |
| IM Address | IM’s logic base address. This address has to match the IM "start address“ in HWConfig of the SIMATIC Manager. Please note that this address has nothing to do with the PROFIBUS address that is set at the IM or the ET200M. |
| IM Channel | Number of the MOBY channel that is to be used for processing: |
|  | ASM Type | Value Range |
|  | IM475, 452, 456,RF170C IM 454, 754, 854 ASM 473, 850 | 1,2, 1,2,3,4 1 |
| command_DB_ number | Number of data block where the MDS command is specified | These INPUT parameters can be changed if ready = 1. After a change of these parameters, init_run does not have to be performed |
| command_DB_ address | Address within the "command_DB“. The next MDS command starts on this address. "command_DB_number“ and "command_DB_address generate a data pointer to the next command (refer to chapter "Configuration Scheme“). |  |
|  | Please note: The input parameters command_DB_number and command_DB_address are to be changed only if ready = 1. After changing these parameters, init_run does not have to be performed. |
| MDS Control | MDS_control switches the attendance check or the MDS control on or off on the IM (refer to chapter "Attendance Check and MDS Control“). |
|  | Value | MDS Control | IM Type |
|  | 0 | Attendance check is switched off. The variable ANZ_MSD_present does not indicate a valid value | All |
|  | 1 | Attendance check is switched on. The MDS control is switched off. The variable ANZ_MDS_present indicates an MDS in the transfer window of a reader | All |
|  | 2 | Attendance check is switched on. The MDS control is switched on and happens by means of the attendance check of the MDS. The NEXT command has to be sent to the IM after each MDS processing. | 454 |
| ECC_mode | Switches on the ECC mode on (true) or off (false). Take note that the ECC mode is permitted only for MOBYI. |
| RESET_long | With the command init_run, all INPUT parameters are transmitted to the IM. For MOBY U/D or RF300 operation, this bit has to be set to true (MOBU_mode = 5) |

Notes

Parameter “ASM_address“ value = 256 (refer to hardware configuration) _________________

Parameter “ASM_channel“ value = 1 for Reader1 _____________________________________

Parameter “ASM_channel“ value = 2 for Reader2 _____________________________________

Parameter “command_DB_number“ value = 47 for both readers _______________________

Parameter “command_DB_address“ value = 0 for Reader1  ____________________________

Parameter “command_DB_address“ Value = 50 for Reader2  ___________________________

Notes

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

Notes

Parameter "option_1“ value = 2 to reset the red flashing of the error LED at the reader with  “Init_Run” ______________________________________________________

__________________________________________________________________________

__________________________________________________________________________

| Variable | Description |
| --- | --- |
| multitag | MOBY U/D or RF300; maximum number of MDS processed in parallel in the field. Permissible values: 1 |
| field_ON_control | MOBY U: BERO operating mode; aerial field is switched on/off automatically. The command "Aerial ON/OFF“ is overlaid by the BERO operating mode. |
|  | 00 hex | = | Without BEROs; no reader synchronization |
|  | 01 hex | = | One or two BEROs; The BEROs are logically ored. While a BERO is operated, the field is switched on |
|  | 02 hex | = | One or two BEROs. The 1st BERO switches the field on and the 2nd BERO switches the field off. If there are 2 BEROs and one field_ON_time is parameterized, the field is switched off automatically if the 2nd BERO does not switch within the BERO time. If no field_ON_time is parameterized, the field remains switched on until the 2nd BERO is operated. |
|  | 03 hex | = | Activate reader synchronization by means of cable connection (refer to manual for Configuration, Installation and Service for MOBY U) |
|  | MOBY D or RF300: 00 hex (reserved) |
| field_ON_time | MOBY U: time for BERO operating mode (field_ON_control = 02) |
|  | 00 hex | = | Time monitoring is switched off. For field switch-off, the 2nd BERO is needed. |
|  | 01 hex .. FF hex | = | 1...255s switch-on time for the Reader field |
|  | MOBY D: MDS type |
|  | 00 hex | = | I-code 1 (for example, MDS D139) |
|  | 01 hex | = | ISO MDS |
|  | RF300: 00 hex (reserved) |
| reserved | Reserved |  |  |

Notes

Parameter “field_ON_time“ value = 0 for MDS type RF300 ___________________________

Parameter “field_ON_time“ value = 1 for MDS type ISO______________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

Command and Status Word "BEST"

The control bits of FB45 are defined in the command and status word.

The command and status word with the variables is generated with UDT 11.

The variables and the associated relative addresses in UDT 11 are shown in the figure below.

Control bits:

The user starts his commands with these Boolean variables.

Control bits from Bit0 to Bit7

| Variable | Description |
| --- | --- |
| cancel | True =interruption of a current command or a command string. FB45 then sets the variable ready. MOBY U/D or RF300: the variable ‘cancel’ is not available. A command has to be canceled with the variable init_run. |
| command_start | True = start of a command or a command string |
| repeat_ command | True = command repetition: The command or command chain stored last in the IM is reprocessed with the next MDS. However, command processing for the MDS is started only after the MDS that was processed has exited the transmission window (ANZ_MDS_present= 0) and a new MDS has entered the transmission window of the reader (ANZ_MDS_present: 0 → 1). False = no command repetition, or command repetition is stopped after the command that was started with the repeat command is processed. Please note that the user has to reset this bit in order to stop command repetition. The result of the command repetition is fetched by the use setting command_start. Repeat_command is not reset automatically by FB45 after the command is processed. The commands init_run and cancel reset the variable repeat_command. This also interrupts a command repetition in the IM. repeat_command can be set again by the application with the next command_start. Handling of command repetition is described in the chapter "Command Repetition“. |
| Init_run | True = IM restart. In this case, FB45 is also reset and the IM re-parameterized. All data and commands in the IM are lost. This bit has to be set in the restart OB (OB100) for each MOBY channel or IM. After a MOBY-IM fault, the error error_MOBY=0F is indicated to the user. The user then has to perform an init_run. Please note: When loading a parameter data block from the programming device to the SIMATIC, bit init_run is pre-assigned TRUE. The result is the automatic execution of an IM restart. The time to execute init_run is normally in the millisecond range. If there is an error, this time may extend to 15s. |
| IM_failure | True = the IM failed. The user sets this bit in OB122 (refer to chapter "Programming Module Failure“). FB45 then signals an error to the user (error_FB = 09) and interrupts the current command. If the user does not program OB122, the PLC enters the STOP mode if the IM fails. |
| FB45_active | FB45 is just processing a command. This variable is set when the command is started (command_start=True) and remains active until FB45 has received the last acknowledgement from the IM The init_run bit was set The cancel bit was set The IM signaled an error |
| ANZ_next | This bit is set if the command executed last was a NEXT command |
| ANZ_reset | This bit indicates that the command executed last was a RESET. The user started the RESET command with "init_run“. |

Notes

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

Control bits from Bit8 to Bit15

| Variable | Description |
| --- | --- |
| ANZ_MDS_present | Indicates the presence of an MDS in the transmission window of the Read/Write MDS. ANZ_MDS_present is indicated only if the user set the INPUT parameter MDS_control. Please note that when init_run is executed, the ANZ_MDS_present indication briefly disappears even if an MDS stays permanently in the transmission window. |
| ANZ_cancel | The command executed last was a command interruption (cancel).The bit is set if the IM displays a cancel acknowledgement by means of the cyclical word (refer to chapter "Cyclical Control Word between Master and MOBY IM“. Reset is automatic by starting a new command. |
| ANZ_ECC | Only MOBY I: If the ECC driver is switched on (INPUT parameter "ECC mode“ = TRUE), the bit indicates that the data read by the MDS was corrected. ANZ_ECC is not an error indication since the data is OK. ANZ_ECC indicates that in the near future the MDS memory that was just processed may completely fail. |
| reserved | Presently not assigned |
| LR_bat | This bit is of significance only if at MOBY I processing takes place with the MDS507. It indicates an empty MDS507 dialog battery. For all other MDSs, this bit can take on any state. |
| battery_low | Only for MOBY I/V with RAM MDS The back-up battery of the RAM MDS is below the threshold. Although it is still possible to process several months at room temperature with the remaining capacity, it is recommended to immediately change the battery or to replace the MDS if the battery can’t be changed. |
| error | FB45 sets this bit if a command is concluded faulty. The error bit is the sum error bit for all occurring errors. The exact cause for the error is located in the variable error_MOBY, error_FB or error_BUS (refer also to chapter "Additional Indications“ or chapter "Error Indications and Error Search“). Restarting the command resets the error bit. |
| ready | Ready indication: after ready = TRUE was indicated, the error bit = FALSE has to be polled. This ensures that the command was processed without error. Please note: The ready bit does not have to be set for starting init_run or cancel. |

Notes

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

Additional indications

The displays indicate to the user the progress of a command.  Error analyses are easy to perform.

| Variable | Description |
| --- | --- |
| IM_busy | This bit is set when the IM processes a command. Normally, "IM_busy“ is inverted to "ready“. IM_busy is indicated by the IM by means of the cyclical word (refer to chapter "Cyclical Control Word between Master and MOBY IM“ under "IM_busy“). If processing takes place with the automatic command start repeat_command, this bit indicates the processing of a new MDS with the command that is to be executed. |
| command_rep_active | The IM is just executing a command repetition. The bit is set as a response to the control variable repeat_command. After init_run, FB45 first resets the command_rep_active; it is set again delayed since FB45 first transmits the MOBY commands to the IM. |
| number_MDS | MOBY U/D or RF300: The number of MDSs is indicated that are presently located in the transmission window. If more than 15 MDSs are in the field, the display number_MDS stops at 0F hex. |
| error_MOBY | The IM signaled this error. As a rule, this error is indicated also on the ERR LED on the IM channel display (refer to chapter "Error Indications and Error Search“). |
| error_FB | Error indication from FB45 (refer to chapter "Error Indications and Error Search“). |
| error_BUS | The transmission path between FB45 and the IM signals an error. As a rule, this is a PROFIBUS error (refer to chapter "Error Indications and Error Search“). This error is indicated by the system functions SFC 58/59. |
| version_MOBY | Display of the firmware version of the MOBY IM. The value entered here is updated after every IM power-up . It is ASCII encoded. Example: DBB26 DBB27 |
|  |  | 31 hex |  | 30 hex | → Version 1.0 |
|  |  | "1“ |  | "0“ |  |

Notes

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

__________________________________________________________________________

All other UDT 11 variables are for internal FB use only.

The user must not change them at all.

## FB10 Reader_Control Program

Now, we are going to program the following in FB10: the control program for the control commands of a reader, and the call of FB45.

In addition, the attendance time of the transponder is to be recorded.

Generating FB10

First, set up a new function block FB10.

Then, set up IN variables

Next, set up OUT variables

Then, set up STAT variables

Next, set up TEMP variables

Networks 1 to 3

Networks 4 to 8

Note regarding networks 7and 8:

The switch-on delay TON (SFB4) in Network 7 and the FB45 call in Network 8 are added as multi-instance. After insertion in the program, click on the block with the right mouse key and select “Change to multi-instance call“.

Then enter the name of the multi-instance in the window (refer to NW7 or NW8 without #).

Save and close FB10

## FB1 Control Program

It is now possible to generate the control program with the completed blocks.

Task:

In our sample program, two command strings with two requests each will be processed.

With the START_SLG1 (I0.0), the command chain of the first reader is executed.

First, the MDS status information will be read, and then a write command is carried out on Reader1. With Reader1, we write 8 bytes that are stored in DB48 starting with DBB0 to the MDS. With the RESET_SLG1 (I0.1), the error is reset if there is an error (LED at Reader1 flashes red) and a “init_run command“ to reset the first reader is executed.

With the RF300_ISO (I02), switching between MDS types (for example RF360T) or ISO transponder (for example, Moby D ISO) is to be carried out on the first reader (RF310R).

With the START_SLG2 (I1.0), the command string of the second reader is executed.

First, the MDS diagnosis information will be read and then a read command will be executed at Reader2. With Reader2, we read 8 bytes from the transponder and then write them to DB48 starting with DBB50.

With RESET_SLG2 (I1.1) the error is reset if there is an error (LED at SLG2 flashes red) and a “init_run command“ is executed to reset the second reader.

In addition, the attendance time of the transponders is to be recorded on the readers.

Supplementing the symbol table

| Symbol | Address | Data Type | Comment |
| --- | --- | --- | --- |
| START_SLG1 | I 0.0 | BOOL | Command start of Reader1 |
| RESET_SLG1 | I 0.1 | BOOL | Reset Reader1 error |
| RF300_ISO | I 0.2 | BOOL | Value 0 = RF300, Value 1 = ISO |
| START_SLG2 | I 1.0 | BOOL | Command start of SLG2 |
| RESET_SLG2 | I 1.1 | BOOL | Reset Reader2 error |
| AWZ_SLG1 | MD 40 | TIME | Attendance time of transponder at SLG1 |
| AWZ_SLG2 | MD 50 | TIME | Attendance time of transponder at SLG2 |
| STATUS_SLG_1 | VAT 1 |  | SLG1 variable table |
| STATUS_SLG_2 | VAT 2 |  | SLG2 variable table |

Generating FB1

Set up a new FB1.

Setting up TEMP Variables

Network 1 to 2

FB10 is inserted as a multi-instance block.

Network 3

Network 4 to 5

Network 6

Save and close FB1

## OB1 Program Call

Double click on OB1 in the project window, or open the object properties of OB1 and enter the symbolic name and the symbol comment.

Open OB1 and call FB1 with DB1

Confirm the window with the query for generating DB1 by clicking on “Yes“.

Save and close OB1

We can now load the program into the controller and test it.

## Variable Table STATUS_SLG_1

## Variable Table STATUS_SLG_2

## Symbol Table

## Block Folder

## DB49 Data View

# Text boxes

UDT11

Byte 50 to Byte 99

to Reader 2

UDT11

Byte 0 to Byte 49

to Reader 1

DB1

Multi-instance DB of FB45

des FB45

FB45

for Reader 2

Per commd UDT21

DB45

a UDT11

integrated

for each reader

DB1

Multi-instance DB of  FB45

des FB45

FB45

for Reader 1

5 Ethernet Connection cONNECTIONVerbindung

Frequency Converter at SIMATIC S7

2 to 3 days Modules H

System Simulation with SIMIT SCE

1 to 2 days Modules G

IT Communication

with SIMATIC S7

2 to3 days Module E

Programming Languages

2 to 3 days Modules C

Process Visualization

2 to 3 days Modules F

3 SIMATIC S7-300 with CPU 315F-2 PN/DP

Additional Functions of

STEP7 Programming

2 to 3 days    Modules B

4 SIMATIC RF180C (ASM)

with reader RF310R (SLG = write/read device)

and transponder RF340T (MDS)

Read MDS Status

Command 0B/02

Industrial Fiedbus Systems

2 to 3 days  Modules D

Read MDS status

Command 0B/01

Fundamentals of

STEP7 Programmig

2 to 3 days      Modules A

DB48

General data

Source data

Destination data

UDT261

DB49 MDS Status

UDT271

Read reader status

Command 04 /01

DB50 Reader Status

Read reader status

Command 04/06

Reader diagnosis

UDT281

UDT111

DB47

1 PC

Write to MDS

Command 01

Read from MDS

Command 02

2 STEP 7

Controller

For example, S7400 CPU

PROFINET IO cable

24V for RF180C and reader (SLG = write/read device)

to additional

PROFINET IO stations

Readout Station

Readout Station

Request or command

Network 1  Command

Network 2  Sub_Command

Network 3  Data Length

Network 6  Destination or target address of the DB of data storage

Network 4  MDS start address

Network 5  DB number for data storage destination or source

Read command, another command follows

Read command, another command follows

Read command, another command follows

Write command, last command in string

Initial Value

Comment

Time value:00-3F

Time factor

Variable

Description

Setting the MOBY Operating Mode

Operating Mode

Value

IM Type

Default

-; reserved for setting with switch or GSD parameterization: different interfaces without switch under- stand under MOBY mode = 0 the  MOBY I_mode.

MOBY I or MOBY E (without MDS 507)

All

MOBY F with MDS F4xx

MOBY U/D or RF300 – without multi tag handling

Res. for MOBY U – with multi tag handling (FB55)

Reserved for MOBY D or  RF300 - with multi tag handling (FB55)

MOBY I  with MDS 507

MOBY F with MDS F1xx

MOBY F (reserved for MDS F2xx) 507

To be noted:

MOBY_mode must only be changed after an IM is switched on

Scannung_time is the scanning time for the MDS 507 of MOBY I and MOBY V. For all other MDS types, the value 00 can be used.here. The figure below shows the setting for the scanning time (refer also to configguration manual for Reader 44/MDS 507):

Example: The result of a scanning time of 1 second  = 81 hex for the parameter ABTA (scanning time)

Relative address in UDT 10

Has to be set by the user

Must absolutely be polled by the user

Optimal scanning bits

Reader block

Command start

Network 1

Network 2  : Reset Reader

Network 3:  ISO mode

Network 4  RF300 mode

Network 5

Network 6  : Attendance time MDS at reader

Network 8  : FB45 call

Network 7  : Reader1 MDS time evaluaton

time evalu

ation

#call_fb45

time