Training Manual for Integrated Automation Solutions

Totally Integrated Automation (TIA)

MODULE E13

VISION SENSOR

Reading Code

with SIMATIC S7-300F-2 PN/DP and VS130-2

This manual was prepared for training purposes by Siemens AG for the project Siemens Automation Cooperates with Education (SCE).

Siemens AG does not guarantee the contents of this document.

Passing on this document as well as copying it, using and communicating its contents is permitted within public training and continued education facilities.  Exceptions require the written permission by Siemens AG (Michael Knust michael.knust@siemens.com).

Violators are held liable to pay damages. All rights -including translation- reserved, particularly if a patent is granted, or a utility model or design is registered.

We wish to thank the Michael Dziallas Engineering corporation and the instructors of vocational schools as well as all those who provided support during the preparation of this manual.

Page

1	Preface	5

2	notes regarding the usage of CPU 315F-2 PN/DP	7

3	notes regarding the VS130-2 components	7

3.1	Product Description	7

3.2	Performance Characteristics	8

3.3	Evaluation Arrangement	8

3.4	Recording and Reading Out Recognition Values in a PROFINET IO Environment	9

3.5	Setting the Communication Interface of the VS130-2 to PROFINET	10

4	starting up a project with CPU 315F-2 PN/DP and VS130-2	12

4.1	Setting Up a New Project	13

4.2	Configuring the hardware	15

4.3	Assigning Device Names	23

4.4	Adding the Block and FB79 to the Project	25

4.5	FB 79 "VS130-2_CONTROL"	25

4.6	Assigning the PROFINET IO Relevant Interfaces of the Evaluation Device	31

4.7	DB20 Result String Data Block	32

4.8	Supplement the Symbol Table	33

4.9	FC10 Control Program	34

4.10	Programming Restarts and Warm Restarts	40

4.11	Calling FC10 in OB1 	41

5	WEB Server based interface of the VS130-2	42

5.1	Setting Up and Evaluating the Model	42

6	results of code evaluation in the CPU	52

6.1	Web View of Code Evaluation	52

6.2	Data View of DB20	52

6.3	Variable Table VAT_VS130	53

The following symbols serve as a guide through Module E13:

Information

Programming

Sample Task

Notes

# Preface

Regarding its content, Module E13 is part of the instruction unit ’IT Communication with S7’.

Objective

In Module E13, the reader learns how networking and data exchange between PLCs and the vision sensor evaluation device VS130-2 is set up.

As PLC, the CPU 315F-2 PN/DP and as vision sensor evaluation device the VS130-2 system is used for reading code.  The SIMATIC VS130-2 components consist of an evaluation device with a sensor head and an LED ring lamp. PROFINET is used for networking between the PLC and the SIMATIC VS130-2.

Module E13 shows in principle the procedure for the startup, based on a brief example.

.

Prerequisites

To successfully work through Module E13, the following knowledge is assumed:

(	How to handle Windows

(	Fundamentals of PLC programming with Step7 (for example, Module A3 ‘Startup’ PLC Programming with STEP7)

(	Fundamentals of network engineering (for example: Appendix V – Basics of Network Engineering)

Hardware and software required

1	PC, operating system Windows XP Professional with SP2 or SP3/Vista 32 Bit Ultimate and Business/Server 2003 SP2 with 600MHz (only XP)/1 GHz and 512MB (only XP)/1 GB RAM, free disk storage approx. 650 to 900 MB, MS Internet Explorer 6.0 and network card

- Software STEP 7 V 5.4

- PLC SIMATIC S7-300 with CPU 315F-2 PN/DP and at least one digital input and output module

Sample configuration:

- Power supply: PS 307 2A

- CPU: CPU 315F-2 PN/DP

- Digital inputs: DI 16x 24VDC

- Digital outputs: DO 16x 24VDC/0.5 A

- SIMATIC VS130-2 evaluation device with sensor head and LED ring lamp

- Ethernet connection between PC, CPU 315F-2 PN/DP and VS130-2.

# notes regarding the usage of CPU 315F-2 PN/DP

The CPU 315F-2 PN/DP is a CPU that is shipped with 2 integrated interfaces.

- The first interface is a combined MPI/PROFIBUS DP interface that can be used at the

PROFIBUS DP as master or slave to connect distributed IO/field devices with very fast reaction time.

In addition, it is possible to program the CPU here by means of an MPI or PROFIBUS DP

- The second interface is an integrated PROFINET interface.

This allows for using the CPU as PROFINET IO controller to operate distributed IO

on PROFINET. The CPU can be programmed by means of this interface also!

- Moreover, it is possible to use fail-safe IO devices on both interfaces.

Notes:

-	In module E13, the CPU 315F-2 PN/DP is used as the controller for the data exchange of a  	SIMATIC RFID system on the PROFINET.

-	To run this CPU, a micro-memory card is required!

- The addresses of the input and output modules can be parameterized at this CPU.

# notes regarding the VS130-2 components

## Product Description

The Vision Sensor SIMATIC VS 130-2 is a code reader for data matrix codes of the type ECC200

(except for the types "Structured Append" and "Reader Programming Code")

as well as the codes PDF417 and QR (except for the types "ECI Code", "Byte Code",

"Kanji Code", "Structured Append" and "FNC1 Code").

The code type is recognized automatically during training and in Adjust, and stored during training as code property.

SIMATIC VS 130-2 processes with the incident light method: the object is illuminated from above with the included ring stroboscopic lamp.  By means of the accessory Lamp Multiplexer, it is possible to select one of up to four lamps for the illumination.

Reading, Comparing and Verifying Code

The SIMATIC VS 130-2 is able to do the following: read codes, compare the entire code or parts of it with a learned code, and relate (verify) the quality values of the code read currently to the quality code of a learned code.

The character chain that was read can be read out either completely or partially (i.e., filtered). Moreover, additional characters can be prefixed or suffixed during the read-out.

The SIMATIC VS 130-2 is able to make good/bad decisions in the stand-alone mode and -within a control process- forward the codes it read.

## Performance Characteristics

• Robust reading of data matrix codes even under more difficult conditions

• Reads printed codes of the type PDF417 and QR on a homogenous background

• Incident light ring flash lamp at VS 130-2

• Control of up to 4 lamps by means of a special lamp multiplexer

• Linking several trained codes that don’t necessarily have to belong to one and the same code type 	       into one code set at VS 130-2

• Specifying a capture range is possible with the VS 130-2

• Operator interface completely Web based

• In the case of data matrix codes, 20 code readings per second

• Determining the quality characteristics

• Extensive operator and monitoring functions, also in the evaluation mode

• Extensive diagnosis and protocol functions: fault profile and event logging

• Firmware update by means of the operator interface

• Control by means of digital I/O, PROFIBUS DP and PROFINET IO, trigger signal in addition by

means of the RS232 interface of an RS232 Ethernet converter or TCP server

• Code pickup without trigger signal ("endless" mode)

• Result output by means of PROFIBUS DP, PROFINET IO, RS232 interface

of an RS232 Ethernet converter, TCP connection on the PC

## Evaluation Arrangement

The objects with the code pass by the sensor head on a suitable conveyor.  During reading, they have to be located completely within the view of the sensor’s field. The character content of the code is stored through training.

The current code is read in the evaluation mode and if applicable compared with the content of the trained code.  The digital output signals are set depending on the result of the reading:

READ (code was localized and decoded)

MATCH (code matches the learned code)

N_OK (code was not readable)

Depending on the parameter assignment, the result of the reading is read out via PROFIBUS DP, PROFINET IO, the RS232 interface of the RS232 Ethernet interface converter or a TCP server.

## Recording and Reading Out Recognition Values in a PROFINET IO Environment

• By means of the Ethernet (TCP/IP) and a switch, a PC/PG is connected that exclusively serves the setup process.

• By means of the Ethernet and a switch, a connection exists with an automation system that has  PROFINET IO capability.

• The automation system controls the SIMATIC VS 130-2.

• The result of the objects to be checked is read out to the automation system by means of         	PROFINET IO.

Additional information is provided in Chapter 1 of the operating instructions

“SIMATIC Vision Sensor VS130-2“.

## Setting the Communication Interface of the VS130-2 to PROFINET

Switch on the power supply of the evaluation device VS130-2 for the initial startup.

At the initial startup, "Factory Settings Used" appears on the LCD display.

Confirm with "OK".

The VS 130-2 will then perform a self test:

• Checking the Ethernet connection

Press ESC

• Functional check of the sensor head

Press ESC

After completion of the self test, "Adjust" appears on the LCD display

Press OK to get to the main menu.

At any additional start of the SIMATIC VS 130-2, the evaluation device VS 130-2 performs the following self test:

• Checking the Ethernet connection

• If needed, checking the connection to PROFINET IO

• If needed, checking the Ethernet RS232 converter or TCP server and to the PC/PG <<?>>

• If needed, checking whether it is possible to exchange data from and to PROFIBUS DP

• Function check of the sensor head

If the self test ran without a fault, the following is indicated on the LCD display: the main menu, the display "Adjust" or the RUN menu, depending on the status at the last switch-off.

You may have to press ESC or OK several times to get to the Main menu.

In addition, we navigate in the LCD display between the menus, and make entries.

"Main" Menu:

To set the VS 130-2 to PROFINET, we have to get to the menu “Connect“.

Place the cursor in front of Connect, and press the OK key.

"Connect" Menu:

The IP mode of the Ethernet has to be set to PNIO.

Place the cursor in front of Ports and press the OK button

Place the cursor in front of Ethernet and press the OK button

Place the cursor in front of IP Mode and press the OK button

Place the cursor in front of PNIO and press the OK button

The evaluation device now requests a restart; press the OK button to confirm.

After the restart, the red bus error LED (BF) flashes until communication is established by means of PROFINET between a controller and the VS 130-2.

ESC may have to be pressed several times to get to the main menu.

All additional information for operating the evaluation device is provided in chapters 4 and 5.2 of the operating instructions “SIMATIC Vision Sensor VS130-2“.

# starting up a project with CPU 315F-2 PN/DP and VS130-2

Below, starting up the VS 130-2 in a project is described.

As SIMATIC S7-300 Station, the CPU 315F-2 PN/DP is used.

In the CPU’s control program, a data structure has to be generated by means of a function block call (FB79) with data block (DB20).

The data structure looks like this:

All additional information is provided in Chapter 6.5 of the operating instructions  “SIMATIC  Vision Sensor VS130-2“.

## Setting Up a New Project

1. 	The central tool n STEP 7 is the  ’SIMATIC Manager’.  Here, we are calling it with a double click. (® SIMATIC Manager)

2. 	STEP 7 programs are managed in projects. We are now setting up such a project

(® File ® New)

3.	The project is assigned the ’Name’ ’VS130-2’ (® VS130-2 ® OK)

- Highlight your project and insert an ’Industrial Ethernet Subnet’

(( VS130-2 ( Insert ( Subnet ( Industrial Ethernet).

- Next, we insert a ’SIMATIC 300 Station’ (® Insert ® Station ® SIMATIC 300 Station)

## Configuring the Hardware

- With a double click, open the configuration tool for ’Hardware’. (® Hardware)

- Open the hardware catalog by clicking on the symbol '’. (® )

With a double click, insert the ’Mounting Channel’ (® SIMATIC 300 ® RACK-300

® Mounting Channel).

Note:

After that, a configuration table for setting up Rack 0 is displayed automatically.

- From the hardware catalog, select all modules that are also present in your rack and insert them in the configuration table. To this end, click on the name of the respective module, hold the mouse key and drag it to a line in the configuration table.

We start with the power supply ’PS 307 5A’ (® SIMATIC 300 ®  PS-300 ® PS 307 5A).

Note:

If your hardware deviates from the one shown here, simply select the corresponding modules in the catalog and insert them in your rack. The order numbers of the individual modules -which are also inscribed on the components-  are shown in the footer of the catalog.

- Next, we drag the ’CPU 315F-2 PN/DP’ to the second slot.

The CPU’s order number and version are inscribed on the front of the CPU.

(® SIMATIC 300 ®  CPU-300 ® CPU 315F-2 PN/DP ® 6ES7 315-2FH13-0AB0 ® V2.6)

- When entering the CPU, the window below appears.  In it, we do the following: assign an ’IP Address’ to the CPU 315F-2 PN/DP, specify the ’Subnet screen form’ and select the ’Ethernet’ that is already set up.  Optionally, a ’Router- address’ can be selected for network overarching communication. Confirm your inputs with ’OK’ (( IP address: 192.168.0.100 ( Subnet screen form: 255.255.255.0 ( Ethernet(1) ( Don’t use a router ( OK)

Notes regarding networking on the Ethernet (additional information is provided in Appendix V of the training manual):

MAC address:

The MAC address consists of a permanent and a variable part. The permanent part ("Basic MAC address") identifies the manufacturer (Siemens, 3COM, ...). The variable part of the MAC address differentiates the different Ethernet stations and should be assigned globally unique. On each module, a MAC address specified by the factory is inscribed.

Value range for the IP address:

The IP address consists of 4 decimal numbers in the value range 0 to 255, separated by a period; for example: 141.80.0.16

Value range for the subnet screen form:

This screen form is used to establish whether a station or its IP address belongs to the local subnet, or can be reached only by means of a router.

The subnet screen form consists of 4 decimal numbers in the value range 0 to 255, separated by a period; for example:  255.255.0.0

The 4 decimal numbers of the subnet screen form have to contain  -in their binary representation- from the left a series of gapless values "1" and from the right a series of gapless values "0"..

The values "1" determine the area of the IP address for the network number. The values "0" determine the area of the IP address for the station address.

Example:

Correct values:	255.255.0.0 Decimal = 1111 1111.1111 1111.0000 0000.0000 0000 binary

255.255.128.0 Decimal = 1111 1111.1111 1111.1000 0000.0000 0000 binary

255.254.0.0 Decimal = 1111 1111.1111 1110.0000 0000.0000.0000 binary

Incorrect value:	255.255.1.0 Decimal = 1111 1111.1111 1111.0000 0001.0000 0000 binary

Value range for the address of the gateway (router):

The address consists of 4 decimal numbers in the value range 0 to 255 separated by a period; for example, 141.80.0.1.

Relationship of the IP addresses, router address and subnet screen form:

The IP address and the gateway address must differ only at those positions where a "0" is shown in the subnet screen form.

Example:

You entered the following: for subnet screen form 255.255.255.0; for IP address 141.30.0.5 and for router address 141.30.128.1.

The value for the IP address and the gateway address is to differ only in the 4th decimal number. However, in the example, the 3rd position already differs.

In the example, we have to alternatively change:

- the subnet screen form to: 255.255.0.0 or

- the IP address to: 141.30.128.5 or

- the gateway address to: 141.30.0.1

- Next, we drag the input module for 16 inputs to the 4th slot. The module’s order number is inscribed on its front (® SIMATIC 300 ® DI-300 ® SM 321 DI16xDC24V).

Note:

Slot 3 is reserved for interface modules and remains empty for that reason.  The module’s order number is shown in the footer of the catalog.

- Now we drag the output module for 16 outputs to the 5th slot. The module’s order number is inscribed on its front.  (® SIMATIC-300 ® DO-300 ( SM 322 DO16xDC24V/0,5A).

Note:

The module’s order number is shown in the footer of the catalog.

- Next, we have to change the PROFINET device name to PN-IOx100.

Select ’PN-IO’ with a double click (® PN-IO,( PN-IOx100,( OK)

- Drag the PROFINET IO System (100) module tier toward the right and from the folder  PROFINET IO add the SIMATIC VS100 module VS130-2 to the tier by dragging it there.

If module VS130-2 should not be available for selection, it has to be inserted with the menu “Extras“ Install GSD files by a data carrier.

- Now, double click on the inserted module and change the device name to  VS130-2x130 and the IP address to 192.168.0.130

- Next, double click on the control byte of the inserted module and change the addresses of the

Inputs to 10, and those of the outputs to 20.

Hardware View

- With a click on '’, the hardware configuration is saved and compiled.

## Assigning Device Names

- Highlight module VS130-2 and then select, by means of the menu “Destination system“ at Ethernet Assign device name.

Note:

The precondition for this is that the PG/PC interface is set for TCP/IP and the PC’s network card is configured correctly.  For example, IP address 192.168.0.99, Subnet 255.255.255.0 and Router address -.-.-.- (refer to Module E02)

- Now highlight the VS100 module and then click on the button “Assign name“. Close the window.

- By clicking on '’, we now can load the hardware configuration into the PLC. The operating mode switch on the CPU should be on Stop! (®  )

(After the hardware is loaded, the red BF LED on the VS130-2) goes off.

- Close the hardware configuration.

## Adding the Block and FB79 to the Project

De-archive and open library VS130-2 from the template directory, or from the

Vision Sensor SIMATIC VS130-2 V2.6 CD in the directory “Function Blocks“.

Add FB79 to the block folder of the project.

Close the library.

Note:

Instead of library VS130-2, the example program VS130-2_Examples can be de-archived. The file VS130_2_Examples.zip is located on the Vision Sensor SIMATIC VS130-2 V2.6 CD in the directory “Examples“, sub-directory “SIMATIC“

## FB 79 "VS130-2_CONTROL"

FB 79 "VS130-2_CONTROL" is used to communicate with the SIMATIC VS 130-2.

You simply specify the request, and the block handles the communication by means of the interfaces opened up in HWConfig, under the incorporation of the PROFINET IO device VS 130- 2.

The following bits of control byte (AB20) have to be processed outside the FB:

• TRG (Trigger): starting the evaluation

• RES (Reset): acknowledging an error (refer to error indications)

In order to get a good/bad reading evaluation, the result bits (EB10) READ, MATCH and N_OK of the status byte have to be evaluated.

Note

In the control byte of the evaluation device, you influence from your program only the bits RES and TRG when using FB79.

The FB influences all other bits of the control byte.

The following requests are possible:

• Cancel the current request (COMMAND =W#16#0000)

• Select code (COMMAND =W#16#0001)

• Train a code (COMMAND =W#16#0002)

• Read out result strings (COMMAND =W#16#0081)

• Read out the position of the code (COMMAND =W#16#0088)

• Read out the quality characteristics of the code that is currently read (COMMAND =W#16#0082)

• Read out the number of the code currently selected (COMMAND =W#16#0003)

• Read out the current operating mode of the VS 130-2 (COMMAND =W#16#0004)

• Reset the control signal DISA (COMMAND =W#16#0005)

For almost all requests, FB79 resets the control signal DISA to TRUE for the VS 130-2. This is to prevent that the VS 130-2 is controlled simultaneously by means of the keyboard, an operator panel or the WEB server based interface of the VS130-2.

The four requests below are an exception:

• Reset the control signal DISA.

• Cancel the current request. The FB does not change DISA.

• Read out the number of the currently selected code. The FB does not change DISA.

• Read out the current operating mode of the VS 130-2. The FB does not change DISA.

Whether a request can be executed successfully depends on the current operating mode of the VS 130-2 (for example, all COMMANDs with W#16#8x are possible only in RUN).

The FB only monitors the true data traffic between the VS 130-2 and the controller; i.e., the parameter DONE provides no indication regarding the actual read result. .

The parameter DONE confirms that a request was completed successfully.

Note

• If you want to read out a result string using FB79, the output of the result string has to be set for

PROFIBUS DP or PROFINET IO.

For the following requests, the evaluation device queries the number of the selected code

-	"Change a code" (COMMAND =W#16#0001),

-	"Train a code" (COMMAND =W#16#0002) and

-	"Read out the currently selected code" (COMMAND =W#16#0003)

For that reason, in these cases also the output of the result string has to be set on PROFIBUS DP or PROFINET IO.

• The interface for the signals DISA, SEL0 to SEL3, TRN, RES, IN_OP, TRD,

RDY always has to be set to PROFIBUS DP or PROFINET IO.

• The setting of the interface for the result bits READ, MATCH, NOK is irrelevant to

FB79 (i.e., these bits can also be placed on the digital outputs of the VS 130-2).

Input Parameters of the FB79

Output Parameters of the FB79

Permissible Values for the Parameter COMMAND

Notes

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

Error Information for the FB79

If an error occurred, ERROR = TRUE is set. The exact cause for the error is indicated in ERRCODE. In addition, there are warnings where ERROR is set to FALSE. They identify an error situation that does not cause the present request to be cancelled.

If after an FB call, ERRCODE <> DW#16#0000 0000, you have to call the FB again with RESET=TRUE in order to reset the error information at the FB.

Note

By calling the FB with RESET=TRUE, you are only acknowledging error indications of the FB. To acknowledge VS 130-2 errors (for example, transmit error), the RES bit of the control byte has to be set.

## Assigning the PROFINET IO Relevant Interfaces of the Evaluation Device

Control Byte

Note

Signals SEL0, SEL1, SEL2, SEL3, TRN and RES have an effect only if DISA=1.

Status Byte

Additional information is provided in Chapter 6.5 of the operating instructions

“SIMATIC Vision Sensor VS130-2“.

## DB20 Result String Data Block

The result string is stored in DB20.

Generate DB20

Open DB 20, set up 500 bytes

Under Name, enter “RESULT“

At Type (with the right mouse key) Combined Data Types select the ARRAY data format.

Enter 1..500 within the brackets.

In the next line, select or enter BYTE.

Save and close DB20.

## Supplement the Symbol Table

Open the symbol table and enter the following symbol assignments.

Save and close the symbol table.

## FC10 Control Program

We are now generating the control program for the Vision Sensor Module VS130-2.

With the START input (I0.0), the command for the image pickup and the code evaluation is executed.  A START is possible only if the VS130-2 is in the RUN mode.

With the RESET input (I0.1), FB79 is reset and initialized, and the VS130-2 is reset if there is an error.

With the RESET_DISA input (I0.2), the control signal DISA is set to FALSE.

With the CHANGE_CODE input (I0.3), the code can be changed.

The CODE_NUMBER of the code to be selected is specified in this case with Input Byte 1 (IB1). Only codes can be selected that have been trained.

With the code TRAIN_CODE input (I0.4), a new code can be trained.

The CODE_NUMBER of the code to be trained is specified with Input Byte 1 (IB1). A maximum of 15 codes (Number 1 to 15) can be trained.

The status bits of the FB79 are displayed in QB4 (outputs Q4.0 to Q4.2).

The status bits and result bits of the VS130-2 are displayed in QB5 (outputs Q5.0 to Q5.5).

When FB79 is called, the input and output addresses of the VS130-2 (hardware) are entered in HEX format at the first four input parameters.

At input parameter RECV, DB20 is specified as ANY P#DB20.DBX0.0 BYTE 500.

Starting with MB20, additional status information of FB79 is read out.

It is possible to monitor this additional status information in the online view or by means of the variable table.

Generate FC10.

Networks 1 to 4

Notes

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

Networks 5 and 6

Notes

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

Networks 7 and 8

Notes

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

Networks 9 to 11

Notes

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

Networks 12 to 15

## Programming Restarts and Warm Restarts

To initialize the FB, we have to set the RESET input of FB79 in OB100.

This input is reset by calling FB79.

Generate and open OB100.

Then, in the symbol table, assign the symbol name "Instanz_DB79“ to DB79.

## Calling FC10 in OB1

Double click on OB1.

Enter the symbolic name and symbol comment.

Confirm with OK.

Enter Network 1.

Save and close OB1.

We can now load the program into the CPU.

# WEB Server based interface of the VS130-2

## Setting Up and Evaluating the Model

Open the Internet browser.

As link, enter the IP address 192.168.0.130 of the VS130-2.

To set the language, click on the German flag.

Next, click on Set Up Sensor.

On the left of the interface, you will see a selection of tasks in the form of buttons.  Activate the desired task with a mouse click on the corresponding button.  The associated dialog will then be displayed on the right side of the interface.

The Web server based interface for Vision Sensor SIMATIC VS130-2 provides the following

dialog fields for image evaluation:

• Set up

• Connections

• Training

• Evaluating

• Options

• Info

• Managing

• Stop

A traffic light is located below the task buttons that shows you at a glance the current operating mode of the evaluation device VS130-2.

The traffic light can display the following states:

• Green: 	Evaluation mode VS130-2 with result output

• Yellow: 	STOP including setup and training

• Red: 	Error

Now click on the button Set up.

In the dialog on the upper left, a static text is displayed that provides brief instructions for setting up the sensor.

Current Image

At "recognition", the status of image recognition is displayed:

• "completed successfully" in blue script if it was possible to decode the code that is read currently

• "running" in red script if it was not possible to decode the code that is currently read at the first try.

Only those images are displayed that the VS 130-2 attempts to evaluate.

The images are shown in a green frame (indication for recognized code).

Result

If a code was decoded successfully, the code that was read last or the modified result string is displayed in the field Result below the image preview. If it was not possible to decode the code, this field is gray.

Quality, Class, Value

If a code was read correctly (recognition: "completed successfully"), the quality characteristics will be displayed here that -at the momentary setup situation- caused most of the problems when the code was read.  By removing these problems, the reading integrity of the VS130-2 can be specifically improved.

Additional information is provided in Chapter 5.3 of the operating instructions

“SIMATIC Vision Sensor VS130-2“.

Now, click on the Connections button.

Then click on the tab Integration or the button Continue.

At Connection, select PROFINET IO for the source, the text, the result, and the controller.

This allows for the access by means of the control program and FB79.

Click Accept.

Now click on the button Train.

Click on the button Start Training.

Then click on the button Save.

Additional information is provided in Chapter 5.3 of the operating instructions

“SIMATIC Vision Sensor VS130-2“.

Next, click on the button Evaluate.

In this dialog we start the evaluation mode.

The codes are read and if necessary checked as to whether they match a trained code, or contain one or several specified character strings.

Select Code

Here, we enter the number of a code that has already been trained and that we wish to use for comparison with a current code. The following values are provided:

• The numbers of all codes that are already trained

• "Auto", if under "Options" in the Decoder we entered "Read" as "Task".

Click on the button Start.

Specify the START command at the SIMATIC controller to start the evaluation.

Note

With the START command at the controller, the DISA signal was set to TRUE. This disables all operator functions at the VS130-2 evaluation device and in the Web browser.

Enter <<?>> the RESET_DISA signal at the SIMATIC controller to cancel the operator inhibit.

Now click on the Options button.

The VS130-2 is still in the evaluation mode.

Click on the button Stop and confirm with Yes.

We now can make further settings.

Click on the button Options. Under Task select “Compare“.

Click on Accept.

Then click on Evaluate and start the evaluation mode.

Enter the START command at the SIMATIC controller to start code evaluation.

The recorded code was compared with trained Code 1. We have a match.

The outputs READ and MATCH are briefly activated on the VS130-2 and on the controller.

Evaluate another code.

The codes don’t match. A comparison error occurred. The result of the code evaluation is read out with the supplement Match Err in parentheses.

The output READ is activated briefly on theVS130-2 and the controller.

If the code is faulty or illegible, Read Err is read out.

The output N_OK is briefly activated on the VS130-2 and on the controller.

View of Info Statistical Information

View of Info Trained Codes

Additional information is provided in Chapter 5.3 of the operating instructions

“SIMATIC Vision Sensor VS130-2“.

# results of code evaluation in the CPU

## Web View of Code Evaluation

## Data View of DB20

## Variable Table VAT_VS130

# Text boxes

Power Supply Cable

Function Ground Cable

PC/PG for Setup Support

Automation System

Evaluation Device

DB20

Result of code evaluation

Instance DB79

of FB79

FB79

for VS130-2

5 Ethernet connection

Frequency Converter at SIMATIC S7

2 to 3 days  Modules H

System Simulation

with SIMIT SCE

1 to 2 days  Modules G

IT Communication

with SIMATIC S7

2 to 3  days  Modules E

Programming Languages

2 to 3 days Modules C

Process Visualization

2 to 3 days  Modules F

3 SIMATIC S7-300 with CPU 315F-2 PN/DP

Additional Functions of

STEP7 Programming

2 to 3 days    Modules B

4 SIMATIC VS130-2

with sensor head and LED ring lamp

Industrial Fieldbus Systems

2 to 3 days Modules D D

Sensor head with ring flash lamp

Fundamentals of

STEP7 Programming

2 to 3 days     Modules A

Power Supply

1 PC

Object

Light barrier

2 STEP 7

Sensor Cable

Lighting Cable

Sensor Head

LED Ring Lamp

Light Barrier

Object

Cable DI/DO

Conveyor

Conveying Direction

Sensor Head

LED Ring Lamp